## Slide 1
Project：433MHz RF Remote Control
Remote control motor on/off and LED on/off with a pair of 433MHz Tx/Rx modules

## Slide 2
433MHz Transmitter side:
BM53A367A BMduino UNO
BMC21M041 433MHz OOK Tx
BMK52M134 4-key capacitive touch module
Material
433MHz Receiver side:
BM53A367A BMduino UNO
BMC23M041 433MHz OOK Rx
BMP73T102 motor driver shield
DC motor
LED

## Slide 3
Wire Connection – Tx side
Connection
Connect BMC21M041 to BMCOM1 of the BMduino UNO board
Connect BMK52M134 to BMCOM2 of the BMduino UNO board
Program code
BMC21M041_TX.ino

## Slide 4
Wire Connection – Rx side (1)
Connection
Connect BMC23M041 to BMCOM1 of the BMduino UNO board
Connect BMP73T102 (motor driver shield) to the BMduino UNO board
Connect DC motor to BMP73T102
Connect an LED (with resistor for current limit) to D13 pin of BMP73T102
Program code
BMC23M041_RX_2CH_DcMotor.ino
DC
D13

## Slide 5
Wire Connection – Rx side (2)
Stepper
D13
Connection
Connect BMC23M041 to BMCOM1 of the BMduino UNO board
Connect BMP73T102 (motor driver shield) to the BMduino UNO board
Connect stepper motor to BMP73T102
Connect an LED (with resistor for current limit) to D13 pin of BMP73T102
Program code
BMC23M041_RX_4CH_StepperMotor.ino

## Slide 6
Video - pairing
Pairing：
After the RX side is powered on, it will enter pairing mode, and the LED will flash. Press any Key (except Key3) on the TX side to complete pairing.
→ pairing success：LED turns off
→ pairing failure：LED turns on

## Slide 7
Video – DC motor
Key1: motor runs
Key2: motor stops
Key3: LED flash
Key4: LED off

## Slide 8
Video – Stepper motor
Key1: motor runs
Key2: motor stops
Key3: LED flash
Key4: LED off

## Slide 9
END