## Slide 1
Project：433MHz RF Remote Control
Use the BMC36M041 433MHz FSK module
Remote control of a 7-segment display with a slide touch sensor

## Slide 2
Material
Both the 433MHz Transmitter side and Receiver side :
BM53A367A BMduino UNO
BMC36M041 433MHz FSK Transceiver module
BMK54T004 4-key and slide capacitive touch sensing shield
BMD11M134 4-digit Alphanumeric Display Module

## Slide 3
Wire Connection
Connection
Connect BMC36M041 to BMCOM1 of the BMduino UNO board
Connect BMD11M134 to BMCOM2 of the BMduino UNO board
Connect BMK54T001 shield to the BMduino UNO board
Program code
BMC36M041_TRX.ino

## Slide 4
Pairing is required for first time use.
STEP1: Press KEY1 on both sides to enter the pairing mode, the MRX led flashes.
STEP2: Press KEY2 on either side to transmit the pairing packet, when the pairing is completed, the MRX led stops flashing. And the alphanumeric display are lit up.
Once the pairing is completed, no pairing is required in subsequent use.
Video - pairing
Determine whether it
has been paired before:
Check the alphanumeric
display when powering on.
ON: displaying 0, it has been paired.
OFF: not paired before

## Slide 5
Press any KEY and then touch the slide within 5 seconds, the corresponding LED digit will display the value of the slide position.
Video – function demonstration

## Slide 6
Clear pairing: press all keys (KEY1 to KEY4) at the same time. The display will be OFF.
Re-pairing: follow the steps described on page 4.
Video – clear and re-pairing

## Slide 7
END